## Slide 1: Peak Detection in Time Series
Presentation of Final Results
Nestor Weidemann, Nathira Wijemanne
Autonomous Multisensor Systems Group
Institute for Intelligent Cooperating Systems
Faculty of Computer Science
Otto von Guericke University Magdeburg
16.09.2025

## Slide 2
1.
Introduction
2.
Methodology
3.
Results
4.
5.
Evaluation
Conclusion
Peak Detection in Time Series | N. Weidemann

## Slide 3
Motivation
Sustainability and energy efficiency
Computer Numerical Control (CNC) machines are widely used in modern manufacturing
1. Introduction
2.
3.
4.
5.
[1]
Peak Detection in Time Series | N. Weidemann
Notes: Automated production processes are industry standards
Energy efficiency and machine longevity affect on environmental and economic performance
A milling machine is a tool that uses rotating cutting bits to remove material from a workpiece, shaping it into precise dimensions and features
A CNC machine automates this process by following programmed instructions, allowing for highly accurate and repeatable machining of complex parts

## Slide 4
Consequences
Stress on the drive electronics, leading to a reduced motor lifespan
Increase in energy consumption
Problem
Sudden power surges can occur in the motor current of a milling machine
1. Introduction
2.
3.
4.
5.
[2]
Peak Detection in Time Series | N. Weidemann
Notes: Important to distinguish between normal power increases (e.g. caused by the tool engaging with material) and abnormal peak anomalies

## Slide 5
Task
Implement and compare different approaches for peak detection
Goal
Identify sudden power surges
Detect anomalies or inefficiencies
1. Introduction
2.
3.
4.
5.
[3]
Peak Detection in Time Series | N. Weidemann
Notes: Use Case: Milling Machine
The information can then be used to find errors in the G-Code

## Slide 6
Analysis of peak characteristics
1. Introduction
2.
3.
4.
5.
Peak Detection in Time Series | N. Weidemann
Notes: Peaks can have different shapes and widths

## Slide 7
1.
Introduction
2.
Methodology
3.
Results
4.
5.
Evaluation
Conclusion
Peak Detection in Time Series | N. Weidemann

## Slide 8
Multivariate (and non-linear) methods
Univariate (and linear) methods
1.
2. Methodology
3.
4.
5.
Threshold-Based
Moving-Average
Wavelet Transform
K-Means
DBSCAN
Isolation Forest
Autoencoder
Broad variety of techniques from simple to complex and data-driven
Peak Detection in Time Series | N. Weidemann
Notes: Linear methods assume a linear relationship or operate via linear operations
Nonlinear methods model complex, nonlinear relationships
Univariate methods analyze one time series at a time
Multivariate methods can consider multiple dimensions/features simultaneously

## Slide 9
General Overview of Pipeline
1.
2. Methodology
3.
4.
5.
Data Processing
Model Building
Model Tuning
Visualization
Evaluation
Pseudo Labeling
Peak Detection in Time Series | N. Weidemann

## Slide 10
Threshold-Based Approach
A point is identified as a peak if:
  It is a local maximum
  Its value exceeds a threshold
  Its prominence exceeds a threshold
1.
2. Methodology
3.
4.
5.
Peak Detection in Time Series | N. Weidemann
Input-Feature-Variants
Torque with removed DC-offset
Absolute gradient of the command-speed
[4]
Notes: Parameters: value-threshold, prominence-threshold
Prominence measures how much a peak stands out from surrounding valleys
A peak's prominence is the vertical distance between the peak and the lowest contour line that surrounds it and contains no higher peak
Higher prominence = more significant or isolated peak
Local maximum check: implicitly a window-size of 3
commanded speed: speed setpoint from the trajectory planner to the motor controller

## Slide 11
Moving-Average-Based Approach
1.
2. Methodology
3.
4.
5.
Peak Detection in Time Series | N. Weidemann
Apply Moving-Average-Smoothing
Determine the difference to the original signal
Check for local maxima that exceed the threshold
Notes: Parameters: window size, threshold for peak
Input feature: torque

## Slide 12
Wavelet Transform
Using the Ricker wavelet as a basis function
Scale the wavelet and apply convolution on the target signal
High response indicates strong similarity
1.
2. Methodology
3.
4.
5.
Peak Detection in Time Series | N. Weidemann
[5, 6]
Notes: Parameters: width/scale of the wavelet, (response-percentile)
Scipy considers every response in the lower 10th-percentile as noise
Convolution: shift -> normalize (local) -> dot-product
Matrix: coefficients across different scales (frequencies) and positions (time)
Peaks appear as strong, aligned coefficients across multiple scales
Scipy uses a signal-to-noise ratio logic implicitly to judge peak strength

## Slide 13
Clustering with K-Means
1.
2. Methodology
3.
4.
5.
Peak Detection in Time Series | N. Weidemann
Training an autoencoder
Using Encoder to transform inputs into latent-space
Randomly initialize K centroids
Recompute the centroids by calculating the mean of all points assigned to it
Assign each point to the nearest centroid
[7]
Notes: Parameters: number of clusters “k”
Autoencoder tries to reproduce the input
Repeat until changes in cluster assignments are minimal
Partitioning the data into k groups based on minimizing the distance between points and their assigned cluster centroids

## Slide 14
Clustering with DBSCAN (Density-Based Spatial Clustering of Applications with Noise)
1.
2. Methodology
3.
4.
5.
Peak Detection in Time Series | N. Weidemann
Training an autoencoder
Using Encoder to transform inputs into latent-space
Grouping together points that are closely packed
Marking those as outliers that lie alone in low-density regions
[7]
Notes: Parameters: epsilon controls the radius of neighborhood (distance threshold)

## Slide 15
Isolation Forest
1.
2. Methodology
3.
4.
5.
Outlier
Regular data point
Create random splits to isolate all data points
Compute the anomaly score
Determine the outliers using a threshold for the score
Peak Detection in Time Series | N. Weidemann
Notes: Key parameter: contamination, number of trees
Uses Extremely Randomized Tree Regressors to separate anomalies from the rest of the data
Calculates an anomaly score for each data point and checks with a threshold. score depends on avg path length of an isolated point and average depth of all data points. closer to 1, strong anomaly
Does not assume the distribution
However, not built for timeseries data

## Slide 16
1.
2. Methodology
3.
4.
5.
Peak Detection in Time Series | N. Weidemann
Encoder
Latent space
Decoder
Training an autoencoder
Compute the reconstruction error
Identify peaks based on a threshold for the error
Autoencoder
Notes: An autoencoder is a neural network model that seeks to learn a compressed representation of an input, known as the latent space. And the decoder tries to recreate the features based on the compressed representation. The goal is to minimize the difference between the original and reconstructed data.
Long Short-Term Memory, or LSTM, network are specifically designed to support sequences of input data.
If the reconstructed output is different from the original input, it can show an anomaly or outlier which makes autoencoders useful for fraud detection and system monitoring.
LSTM training is slower than CNNs
Hyperparameters: Number of layers/units, Sequence length, Learning rate, Dropout Batch size
Other parameters: reconstruction error threshold  IQR/percentile etc.
Detects anomalies for multivariate timeseries data by learning non-linear patterns
LSTMs – designed for sequences

## Slide 17
Determining the parameters
The quality of the parameters is estimated purely from statistical metrics:
  Total number of peaks
  Mean peak height
  Mean peak prominence
  Count of sequences without peaks
Using Pareto-Front-Analysis to select the best solution
1.
2. Methodology
3.
4.
5.
Peak Detection in Time Series | N. Weidemann
[8]
Notes: No ground truth available
Multi-Objective Optimization with Pareto-Front
Reason for use: majority of people use this in papers
Count of sequences without peaks -> indicating missed detections
Total number of peaks -> indicating sensitivity
Average peak height -> indicating proportion of true-positives
Average peak prominence -> indicating significance of the peaks

## Slide 18
1.
Introduction
2.
Methodology
3.
Results
4.
5.
Evaluation
Conclusion
Peak Detection in Time Series | N. Wijemanne

## Slide 19
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Wijemanne
Method | Features | Parameters |  | PC | MH | MP | SWP
Threshold-Based | Torque | Threshold = 5 | Min-Prominence = 1.1 | 2977 | 5.03 | 0.89 | 0
Threshold-Based | Cmd.-Speed | Threshold = 0.7 | Min-Prominence = 1.1 | 660 | 6.74 | 0.13 | 0
Moving-Average | Torque | Window = 1250 | Threshold = 2.0 | 56111 | 1.89 | 0.13 | 1
Wavelet Transform | Torque | Min-Width = 100 | Max-Width = 150 | 4964 | 0.88 | 0.05 | 0
K-Means | Cmd.-Speed | K-Clusters = 2 |  | 365670 | 1.2 | 0.09 | 0
DBSCAN | Torque | Epsilon = 3.5 |  | 91936 | 3.2 | 0.16 | 0
Isolation Forest | Torque | Estimators = 100 | Contamination = 0.01 | 73476 | 4.37 | 0.08 | 0
Autoencoder | All inputs | Latent Dims = 8 | Contamination = 0.01 | 33600 | 0.03 | 2.85 | 0
PC: Peak-Count MH: Mean Height MP: Mean Prominence SWP: Sequences Without Peaks
Notes: Optimal compromise between all metrics
Best tradeoff between amplitude and prominence with a more realistic peak count

## Slide 20
Threshold-Based Detection (Torque)
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Wijemanne
Notes: Good precision on easy examples with large outliers but fails on others with many false-positives -> bad generalization
Few true peaks were undetected
Predicting one precise position and not an area
Can detect positive and negative peaks

## Slide 21
Threshold-Based Detection (Cmd.-Speed)
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Wijemanne
Notes: Very high precision -> no false-positives
Most of the true peaks were detected but not all (especially peaks with a smaller amplitude)
Predicting one precise position and not an area
Can detect positive and negative peaks

## Slide 22
Moving-Average-Based Detection
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Wijemanne
Notes: Identifies most of the peaks
Was only unable to properly detect a specific pattern – brings down average of metrics
bad generalization, if threshold can be specified for each machine type, would work better.
Can detect positive and negative peaks

## Slide 23
Wavelet Transform
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Wijemanne
Notes: Very bad precision -> many false-positives
Most of the true peaks were detected but not all
Predicting one precise position and not an area
Can detect only positive peaks (with one single wavelet)
Possible reasons of failure:
  Peaks have different shapes and widths
  Shape is indistinguishable from noise

## Slide 24
Clustering with K-Means
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Wijemanne
Notes: False-positives issues on some sequences
Many peaks were undetected
Unreliable predictions
Can detect positive and negative peaks
Marking the whole peak area instead of just one precise position

## Slide 25
Clustering with DBSCAN
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Wijemanne
Notes: High precision -> almost no false-positives
Some peaks were not detected
Recognizable tendency of detecting peaks
Marking the whole peak area instead of just one precise position
Can detect positive and negative peaks

## Slide 26
Isolation Forest
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Wijemanne
Notes: Not many false-positives issued on the sequences
Many peaks were not detected
Characteristic of marking the whole peak area instead of just one precise position
Can detect positive and negative peaks

## Slide 27
Autoencoder
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Wijemanne
Notes: High precision
Not many false-positives issued on the sequences
Many peaks were not detected
Can detect positive and negative peaks
Detects smaller deviations but sometimes unable to identify larger deviations -> not good

## Slide 28
1.
Introduction
2.
Methodology
3.
Results
4.
5.
Evaluation
Conclusion
Peak Detection in Time Series | N. Wijemanne

## Slide 29
Key criteria
  Precision and recall
  Computational costs and complexity
  Generalization and robustness
  Applicability
1.
2.
3.
4. Evaluation
5.
Peak Detection in Time Series | N. Wijemanne

## Slide 30
Comparison with Pseudo Labels
1.
2.
3.
4. Evaluation
5.
Peak Detection in Time Series | N. Wijemanne
Chart: 
| Threshold- Based (Torque) | Threshold- Based (Cmd.-Speed) | Moving- Average | Wavelet- Transform | DBSCAN | K-Means | Auto- encoder | Isolation Tree
Precision | 0.9031 | 0.71695 | 0.5688 | 0.043923 | 0.48915 | 0.46919 | 0.2159 | 0.4735
Recall | 0.012645 | 0.0072678 | 0.4835 | 0.0029398 | 0.478 | 0.27147 | 0.1265 | 0.3939
F1 | 0.022614 | 0.014305 | 0.3933 | 0.0054127 | 0.42491 | 0.23594 | 0.1543 | 0.3249
Notes: Metrics just show how similar the predictions of each method are with reference to the percentile-approach
Very low recall for all methods that predict precise positions and not an area
Threshold-Based Torque has a higher precision than with Cmd.-Speed because it operates on the same feature as the percentile-approach
  Thus, the prediction are more similar

## Slide 31
Computational Cost, Complexity and Generalizability
1.
2.
3.
4. Evaluation
5.
Peak Detection in Time Series | N. Wijemanne

## Slide 32
Best practice: Threshold-Based Detection
Best results based of visual inspections
Fast computation with low resource allocation
Few parameters to optimize
High precision
1.
2.
3.
4. Evaluation
5.
Peak Detection in Time Series | N. Wijemanne
Notes: Feature-processing forces the user to analyze and understand the data, which can already give some insights into the reason for the anomalies
Drawback: struggles to generalize on unprocessed data with different signal-types (machines, material, etc.)

## Slide 33
1.
Introduction
2.
Methodology
3.
Results
4.
5.
Evaluation
Conclusion
Peak Detection in Time Series | N. Weidemann

## Slide 34
Recommended workflow
1.
2.
3.
4.
5. Conclusion
Peak Detection in Time Series | N. Weidemann
1. Start with a simple method
2. Select and develop suitable input features
3. Optimize the parameters
4. Try a more complex approach
Done
Success
Failure

## Slide 35
Findings
Anomalies are likely caused by sudden changes in the commanded speed
Sharp edges seem to cause the peaks in the current
There seems to be an issue within the planning unit
1.
2.
3.
4.
5. Conclusion
Peak Detection in Time Series | N. Weidemann
Notes: Spindle signal looks like a discrete signal with hard edges (instead of smooth, continuous transitions)

## Slide 36
3 different types of anomalies
Large outlier
Signal flickers to zero
Jumping between quantized levels
1.
2.
3.
1.
2.
3.
4.
5. Conclusion
Peak Detection in Time Series | N. Weidemann

## Slide 37
Ideas for improvement
Consider the width of each peak and its proximity to neighboring peaks
Rescale the signals by a material-specific factor
Cluster formation: peaks that are close to each other are combined
1.
2.
3.
4.
5. Conclusion
Peak Detection in Time Series | N. Weidemann
Notes: Rescale the signals by a material-specific factor to align dynamics in the current caused by normal workload within the same zone to improve generalization
Cluster formation (Coalescence): peaks that are close to each other (within a window distance k) are combined so that only the highest peak remains
(Apply smoothing to the signal to filter noise and remove unsignificant peaks)

## Slide 38: Peak Detection in Time Series
Presentation of Final Results
Thank You For Your Attention!
Nestor Weidemann
Mail: nestor.weidemann@st.ovgu.de
Nathira Wijemanne
Mail: nathira.wijemanne@st.ovgu.de

## Slide 39: References for Graphics
[1] https://www.hubs.com/de/wissensbasis/3d-druck-vs-cnc-bearbeitung/
[2] https://www.fptindustrie.com/deu/
[3] https://www.mdpi.com/1996-1073/17/15/3659
[4] https://en.wikipedia.org/wiki/Topographic_prominence
[5] https://en.wikipedia.org/wiki/Ricker_wavelet
[6] https://www.researchgate.net/figure/Convolution-of-a-signal-with-a-wavelet-function-Part-of-this-figure-is-taken-from-1_fig1_51918746
[7] https://blog.dailydoseofds.com/p/the-limitations-of-dbscan-clustering
[8] https://www.researchgate.net/figure/Pareto-front-distribution-of-the-optimization-problem_fig1_374617028
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: Clustering method -> Hyper parameter tuning
Autoencoder ->
Pseudo labels for evaluation for each approach
Considering efficiency and computational cost when evaluating

## Slide 40: Backup
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 41
F1-Score
Combines precision and recall into one metric
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 42: Dataset
Number of Rows: ~1.6 Million
Time Series data across:
  2 Machine Types (CMX1, DMC2)
  2 Materials (AL, S)
  2 Components (CP1, CP2)
-> 8 different measurements
Variables measured across 4 axes: X (1), Y (2), Z (3) and Spindle (6)
  Target Variable: Current
  Possible Input Variables: Load, Motor shaft positions (actual & desired), Control deviation, Torque, Feedforward velocity, Feedforward torque, Commanded Speed, and etc.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 43: Dataset
Relationships:
  For all axes: Current ∝ Torque
  For all Z: Current ∝ Load (>0.9 correlation)
  Machine CMX1, Spindle: Current ∝ Load (>0.9 correlation)
  Machine DMC2, Y & Z: Current ∝ Encoder Positions (>0.9 correlation)
  Component 2, Y: Current ∝ Load (>0.9 correlation)
  Component 1, Spindle: Current ∝ Load (~0.7 correlation)
Peak Detection in Time Series | N. Weidemann, N. Wijemanne