## Slide 1: Peak Detection in Time Series
Presentation of Final Results
Nestor Weidemann, Nathira Wijemanne
Autonomous Multisensor Systems Group
Institute for Intelligent Cooperating Systems
Faculty of Computer Science
Otto von Guericke University Magdeburg
16.09.2025

## Slide 2: Overview
Slide number “3/…” instead of just “3”
Adapt names in footer depending on who is presenting
Add sources for all “external” graphics
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 3
1.
Introduction
2.
Experimental Setup
3.
Results
4.
5.
Evaluation
Conclusion
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 4
Motivation
Sustainability and energy efficiency
CNC machines are widely used in modern manufacturing
1. Introduction
2.
3.
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: Automated production processes are industry standards
Energy efficiency and machine longevity affect on environmental and economic performance
A milling machine is a tool that uses rotating cutting bits to remove material from a workpiece, shaping it into precise dimensions and features
A CNC (Computer Numerical Control) machine automates this process by following programmed instructions, allowing for highly accurate and repeatable machining of complex parts

## Slide 5
Consequences
Stress on the drive electronics, leading to a reduced motor lifespan
Increase in energy consumption
Problem
Sudden power surges can occur in the motor current of a milling machine
1. Introduction
2.
3.
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: Important to distinguish between normal power increases (e.g. caused by the tool engaging with material) and abnormal peak anomalies

## Slide 6
Task
Implement and compare different approaches for peak detection
Goal
Identify sudden power surges
Detect anomalies or inefficiencies
1. Introduction
2.
3.
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: Use Case: Milling Machine
The information can then be used to find errors in the G-Code

## Slide 7
Analysis of peak characteristics
1. Introduction
2.
3.
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: Peaks can have different shapes and widths

## Slide 8
1.
Introduction
2.
Experimental Setup
3.
Results
4.
5.
Evaluation
Conclusion
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 9
Multivariate (and non-linear) methods
Univariate (and linear) methods
1.
2. Experimental Setup
3.
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Threshold-Based
Moving-Average
Wavelet Transform
DBSCAN
K-Means
Autoencoder
Isolation Forest
Broad variety of techniques from simple to complex and data-driven
Notes: Linear methods assume a linear relationship or operate via linear operations
Nonlinear methods model complex, nonlinear relationships
Univariate methods analyze one time series at a time
Multivariate methods can consider multiple dimensions/features simultaneously

## Slide 10
General Overview of Pipeline
1.
2. Experimental Setup
3.
4.
5.
Peak Detection in Time Series | N. Wijemanne
Notes: Parameters: window size for moving average, threshold for peak

## Slide 11
Threshold-Based Approach
A point is identified as a peak if:
  It is a local maximum
  Its value exceeds a threshold
  Its prominence exceeds a threshold
1.
2. Experimental Setup
3.
4.
5.
Peak Detection in Time Series | N. Weidemann
Input-Feature-Variants
Torque with removed DC-offset
Absolute gradient of the command-speed
Notes: Parameters: value-threshold, prominence-threshold
Prominence measures how much a peak stands out from surrounding valleys
A peak's prominence is the vertical distance between the peak and the lowest contour line that surrounds it and contains no higher peak
Higher prominence = more significant or isolated peak
Local maximum check: implicitly a window-size of 3

## Slide 12
Moving Average-Based Approach
Parameters considered:
  Window size
  Threshold
A point is identified as a peak if:
  It is a local maximum
  Its value exceeds a threshold
1.
2. Experimental Setup
3.
4.
5.
Peak Detection in Time Series | N. Wijemanne
Notes: Parameters: window size for moving average, threshold for peak

## Slide 13
Wavelet-Transform
Using the Ricker wavelet as a basis function
Scale the wavelet and apply convolution on the target signal
High response indicates strong similarity
1.
2. Experimental Setup
3.
4.
5.
Peak Detection in Time Series | N. Weidemann
Notes: Parameters: width/scale of the wavelet, (response-percentile)
Scipy considers every response in the lower 10th-percentile as noise
Convolution: shift -> normalize (local) -> dot-product
Matrix: coefficients across different scales (frequencies) and positions (time)
Peaks appear as strong, aligned coefficients across multiple scales
Scipy uses a signal-to-noise ratio logic implicitly to judge peak strength

## Slide 14
Clustering with K-Means
1.
2. Experimental Setup
3.
4.
5.
Peak Detection in Time Series | N. Weidemann
Training an autoencoder
Using Encoder to transform inputs into latent-space
Randomly initialize K centroids
Recompute the centroids by calculating the mean of all points assigned to it
Assign each point to the nearest centroid
Notes: Parameters: number of clusters “k”
Autoencoder tries to reproduce the input
Repeat until changes in cluster assignments are minimal
Partitioning the data into k groups based on minimizing the distance between points and their assigned cluster centroids

## Slide 15
Clustering with DBSCAN (Density-Based Spatial Clustering of Applications with Noise)
1.
2. Experimental Setup
3.
4.
5.
Peak Detection in Time Series | N. Weidemann
Training an autoencoder
Using Encoder to transform inputs into latent-space
Grouping together points that are closely packed
Marking those as outliers that lie alone in low-density regions
Notes: Parameters: epsilon controls the radius of neighborhood (distance threshold)

## Slide 16
Isolation Forest
Robust for detecting outliers
Does not assume the distribution
However, not built for timeseries data
1.
2. Experimental Setup
3.
4.
5.
Peak Detection in Time Series | N. Wijemanne
Create features (moving averages, lags, variances)
Train Isolation Forest
Score data points and identify peaks
Notes: Key parameter: contamination, number of trees
Uses Extremely Randomized Tree Regressors to separate anomalies from the rest of the data
Calculates an anomaly score for each data point and checks with a threshold. score depends on avg path length of an isolated point and average depth of all data points. closer to 1, strong anomaly
https://www.youtube.com/watch?v=kN--TRv1UDY

## Slide 17
Encoder-Decoder Model
Detects anomalies for multivariate timeseries data by learning non-linear patterns
LSTMs – designed for sequences
High computational cost, requires a lot of hyperparameter tuning, and hard to interpret.
1.
2. Experimental Setup
3.
4.
5.
Peak Detection in Time Series | N. Wijemanne
Train encoder–decoder model
Compute reconstruction error
Identify peaks based on threshold
Notes: An autoencoder is a neural network model that seeks to learn a compressed representation of an input, known as the latent space. And the decoder tries to recreate the features based on the compressed representation. The goal is to minimize the difference between the original and reconstructed data.
Long Short-Term Memory, or LSTM, network are specifically designed to support sequences of input data.
If the reconstructed output is different from the original input, it can show an anomaly or outlier which makes autoencoders useful for fraud detection and system monitoring.
LSTM training is slower than CNNs
Hyperparameters: Number of layers/units, Sequence length, Learning rate, Dropout Batch size
Other parameters: reconstruction error threshold  IQR/percentile etc.

## Slide 18
Determining the parameters
Since no ground truth is available, the quality of the parameters is estimated purely from statistical metrics:
  Total number of peaks
  Mean peak height
  Mean peak prominence
  Count of sequences without peaks
Using Pareto-Front-Analysis to select the best solution
1.
2. Experimental Setup
3.
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Explain pareto front analysis -> visualization of example
Reason for use: majority of people us this in papers
Notes: Multi-Objective Optimization with Pareto-Front
Count of sequences without peaks -> indicating missed detections
Total number of peaks -> indicating sensitivity
Average peak height -> indicating proportion of true-positives
Average peak prominence -> indicating significance of the peaks

## Slide 19
1.
Introduction
2.
Experimental Setup
3.
Results
4.
5.
Evaluation
Conclusion
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 20
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Method | Features | Parameters |  | PK | MH | MP | PS | F1
Threshold-Based | Torque | Threshold = 5 | Min-Prominence = 1.1 | 2,977 | 5.03 | 0.89 | 0 | 
Threshold-Based | Cmd.-Speed | Threshold = 0.7 | Min-Prominence = 1.1 | 660 | 6.74 | 0.13 | 0 | 
Moving-Average | Not app. | Window = 1250 | Threshold = 2.0 | 56,111 | 1.89 | 0.13 | 1 | 0.40
Wavelet-Transform | Torque | Min-Width = 100 | Max-Width = 150 | 4,964 | 0.88 | 0.05 | 0 | 
DBSCAN | Torque | Epsilon = 3.5 |  | 91,936 | 3.2 | 0.16 | 0 | 
K-Means | Cmd.-Speed | K-Clusters = 2 |  | 365,670 | 1.2 | 0.09 | 0 | 
Autoencoder | All cols. | Latent Dims = 8 | Contamination = 0.01 | 33,600 | 0.03 | 2.85 | 0 | 0.15
Isolation Forest | Torque | Estimators = 100 | Contamination = 0.01 | 73,476 | 4.37 | 0.08 | 0 | 0.25
*PK – Peak Count MH – Mean Height MP – Mean Prominence PS – Peakless Sequences F1 – F1 Score based on pseudo labels
Notes: Optimal compromise between all metrics
Best tradeoff between amplitude and prominence with a more realistic peak count

## Slide 21
Threshold-Based Detection (Torque)
Good precision on easy examples
Few true peaks were undetected
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: Good precision on easy examples with large outliers but fails on others with many false-positives -> bad generalization
Predicting one precise position and not an area
Can detect positive and negative peaks
Example-pictures: Seq2 ax1 Seq5 ax1

## Slide 22
Threshold-Based Detection (Cmd.-Speed)
Very high precision
Most of the true peaks were detected
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: No false-positives
Most of the true peaks were detected but not all (especially peaks with a smaller amplitude)
Predicting one precise position and not an area
Can detect positive and negative peaks
Example-pictures: Seq2 ax1 Seq5 ax1

## Slide 23
Moving Average-Based Detection
Good precision on easy examples
Minor peaks were undetected
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: Good precision on easy examples with large outliers but fails on others with many false-positives -> bad generalization
Predicting one precise position and not an area
Can detect positive and negative peaks
Example-pictures: Seq2 ax1 Seq5 ax1

## Slide 24
Wavelet Transform
Very bad precision
Most of the true peaks were detected but not all
Possible reasons of failure:
  Peaks have different shapes and widths
  Shape is indistinguishable from noise
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: Many false-positives
Predicting one precise position and not an area
Can detect only positive peaks (with one single wavelet)
Example-pictures: Seq2 ax1 Seq5 ax1

## Slide 25
Clustering with DBSCAN
High precision
Some peaks were not detected
Recognizable tendency of detecting peaks
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: Almost no false-positives
Marking the whole peak area instead of just one precise position
Can detect positive and negative peaks
Example-pictures: Seq2 ax1 Seq5 ax1

## Slide 26
Clustering with K-Means
False-positives issues on some sequences
Many peaks were undetected
Unreliable predictions
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: Can detect positive and negative peaks
Marking the whole peak area instead of just one precise position
Example-pictures: Seq2 ax1 Seq5 ax1

## Slide 27
Isolation Tree
Not many false-positives issued on the sequences
Many peaks were not detected in selected sequences
Characteristic of marking the whole peak area instead of just one precise position
Can detect positive and negative peaks
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 28
Autoencoder
Not many false-positives issued on the sequences
Many peaks were not detected
Can detect positive and negative peaks
Detects smaller deviations but sometimes unable to identify larger deviations  not good
Least performant method
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 29
Autoencoder - LSTM
Not many false-positives issued on the sequences
Many peaks were not detected
Can detect positive and negative peaks
Detects smaller deviations but sometimes unable to identify larger deviations  not good
Least performant method
1.
2.
3. Results
4.
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 30
1.
Introduction
2.
Experimental Setup
3.
Results
4.
5.
Evaluation
Conclusion
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 31
Key Criteria
  Applicability
  Computational costs / speed / complexity
  Precision and Recall
  Robustness and Generalization
1.
2.
3.
4. Evaluation
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Draft
Notes: It is common to manually checking each sample if it is challenging to generate ground truth data
Examples:
  Robust multi-lane detection and tracking using adaptive threshold and lane classification
  Robust lane detection and tracking with RANSAC and Kalman filter: „defining a ground truth for the data is extremely tedious; hence, it is commonly avoided. Consequently, detections were qualitative and based purely on visual inspection by single user”

## Slide 32
Best solution: Threshold-Based Detection
Feature-processing forces the user to analyze and understand the data, which can already give some insights into the reason for the anomalies
Fast computation with low resource allocation
Few parameters to optimize
High precision and recall if the processed input feature is suitable
Struggles to generalize on raw peak data
1.
2.
3.
4. Evaluation
5.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Draft

## Slide 33
1.
Introduction
2.
Experimental Setup
3.
Results
4.
5.
Evaluation
Conclusion
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 34
Recommended workflow
Start with a simple method
Develop suitable input features
Optimize the parameters
Continue with a more complex approach
1.
2.
3.
4.
5. Conclusion
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Draft

## Slide 35
Findings
Anomalies are likely caused by sudden changes in the commanded speed (speed setpoint from the trajectory planner to the motor controller)
Sharp edges in the speed setpoint seem to cause the peaks in the current
There seems to be a bug within the planning unit
  Spindle signal looks like a discrete signal with hard edges (instead of smooth, continuous transitions
1.
2.
3.
4.
5. Conclusion
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Draft

## Slide 36
3 different types of anomalies
Large outlier
Signal flickers to zero
Jumping between quantized levels
1.
2.
3.
1.
2.
3.
4.
5. Conclusion
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 37
Ideas for improvement
Rescale the signals by a material-specific factor to align dynamics in the current caused by normal workload within the same zone to improve generalization
Consider both the width of each peak and its proximity to neighboring peaks
Apply smoothing to the signal to filter noise and remove unsignificant peaks
Coalescence (cluster formation): peaks that are close to each other (within a window distance k) are combined so that only the highest peak remains
1.
2.
3.
4.
5. Conclusion
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 38: Peak Detection in Time Series
Presentation of Final Results
Thank You For Your Attention!
Nestor Weidemann
Mail: nestor.weidemann@st.ovgu.de
Nathira Wijemanne
Mail: nathira.wijemanne@st.ovgu.de

## Slide 39: References for Graphics
[1] https://www.hubs.com/de/wissensbasis/3d-druck-vs-cnc-bearbeitung/
[1] https://www.fptindustrie.com/deu/
[2] https://www.mdpi.com/1996-1073/17/15/3659
[3] https://en.wikipedia.org/wiki/Ricker_wavelet
[4] https://link.springer.com/article/10.1007/s10950-019-09845-y https://www.researchgate.net/figure/Convolution-of-a-signal-with-a-wavelet-function-Part-of-this-figure-is-taken-from-1_fig1_51918746
[5] https://en.wikipedia.org/wiki/Topographic_prominence
[6] https://blog.dailydoseofds.com/p/the-limitations-of-dbscan-clustering
[7]
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: Clustering method -> Hyper parameter tuning
Autoencoder ->
Pseudo labels for evaluation for each approach
Considering efficiency and computational cost when evaluating

## Slide 40: References for Graphics
[8] https://waterprogramming.wordpress.com/tag/pareto-dominance/
[9]
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: Clustering method -> Hyper parameter tuning
Autoencoder ->
Pseudo labels for evaluation for each approach
Considering efficiency and computational cost when evaluating

## Slide 41: Backup
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 42: Dataset
Number of Rows: ~1.6 Million
Time Series data across:
  2 Machine Types (CMX1, DMC2)
  2 Materials (AL, S)
  2 Components (CP1, CP2)
-> 8 different measurements
Variables measured across 4 axes: X (1), Y (2), Z (3) and Spindle (6)
  Target Variable: Current
  Possible Input Variables: Load, Motor shaft positions (actual & desired), Control deviation, Torque, Feedforward velocity, Feedforward torque, Commanded Speed, and etc.
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 43: Dataset
Relationships:
  For all axes: Current ∝ Torque
  For all Z: Current ∝ Load (>0.9 correlation)
  Machine CMX1, Spindle: Current ∝ Load (>0.9 correlation)
  Machine DMC2, Y & Z: Current ∝ Encoder Positions (>0.9 correlation)
  Component 2, Y: Current ∝ Load (>0.9 correlation)
  Component 1, Spindle: Current ∝ Load (~0.7 correlation)
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 44: Intermediate Results
Sensitivity analysis was done for each technique to identify model that is best suited
Pseudo labels were used for metric calculation and evaluation
Metrics used:
  F1 Score (using Pseudo labels)
  Count of sequences with no peaks
  Total number of peaks
  Average peak height
  Average peak prominence
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: · The prominence of a peak measures how much the peak stands out due to its intrinsic height and its location relative to other peaks. It's not just how high the peak is, but how independent it is from nearby peaks.

## Slide 45: Explanation of the approaches
Isolation Forest
Uses Extremely Randomized Tree Regressors to separate anomalies from the rest of the data
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: Calculates an anomaly score for each data point and checks with a threshold. score is depends on avg path length of an isolated point and average depth of all data points. closer to 1, strong anomaly https://www.youtube.com/watch?v=kN--TRv1UDY

## Slide 46: Results – Isolation Tree
Selected parameters
Features: Torque, Moving Average of Torque as input
Parameters:
  Contamination: 0.01
  Number of estimators: 100
Higher median F1 score (against pseudo labels ) and more realistic peak count
However, better results for certain sequences  Not very generalizable
Peak Detection in Time Series | N. Weidemann, N. Wijemanne

## Slide 47: Explanation of the approaches
Autoencoder Model
Peak Detection in Time Series | N. Weidemann, N. Wijemanne
Notes: Encoder: The encoder takes the input data (e.g., an image, a sound clip, or a text document) and compresses it into a lower-dimensional representation, known as the latent space or encoded representation.
Decoder: The decoder takes the compressed representation and tries to reconstruct the original input. The goal is to minimize the difference between the original and reconstructed data.
If the reconstructed output is different from the original input, it can show an anomaly or outlier which makes autoencoders useful for fraud detection and system monitoring.
https://towardsdatascience.com/auto-encoder-what-is-it-and-what-is-it-used-for-part-1-3e5c6f017726/

## Slide 48: Results – Autoencoder
Selected parameters
Features: Torque as input
Parameters:
  Contamination: 0.01
  Latent dims: 8
  Epochs: 50
  Batch size: 64
Peaks were not detected at all in some sequences
However, good results for certain sequences  Not very generalizable
Peak Detection in Time Series | N. Weidemann, N. Wijemanne